## Slide 1
HP-WAN On-line Meeting
Daniel Huang, ZTE
9th, January, 2025

## Slide 2
After the HP-WAN BoF meeting
Agreed HP-WAN requirements:
1) high-speed data transfer over WANs;
2) scheduling of both the host and the network.
Developed Problem I-D (draft-xiong-hpwan-problem-statement-00) to capture comments and presentations during the BoF meeting
  through consensus we narrowed problem space;
  updated to -01 version based on the comments and discussion on the hp-wan mailing list.

## Slide 3
Requirements for HP-WAN
Requirements at BoF meeting and mailing list:
  Massive data transmission, high-volume data with high-speed transfer, e.g. the data speed of a flow could be at 2Gbps~1Tbps.
  Requested completion time, the data transmission should be completed within a requested completion time, e.g. the completion time could be at minutes~milliseconds.
  Scheduled transmission, traffic patterns could be scheduled by the sender, e.g. data volume, start time, finish time, service type.
  Long-distance transmission over non-dedicated WANs, with multiple hops and domains, long RTT latency, routing changes, network congestion, packet loss and link quality fluctuations.
  Multiple flows should be able to co-exist over WANs.

## Slide 4
Technical Goals for HP-WAN
Goals based on discussion and use cases discussed on list and at IETF 121 BOF
  Primary Goal: Completion Time
    The completion time for some applications should be at seconds or minutes.
    The deviation of completion time for multiple concurrent flows should be within seconds to avoid the long tail effect.
  Performance Goals :
    High throughput: ensuring the high-speed data transmission within a requested completion time for a flow, which could be impacted by the bandwidth, convergence speed, start time and RTT.
    Efficient use of capacity: efficiently using available network capacity with fairness to maximize data transfer rates and minimize the completion time for multiple flows.

## Slide 5
Problem 1: Completion Time cannot be met
  The host performs blind transmission and adjusts sending rates by overloaded links detection such as reacting to packet loss and congestion or estimating available bandwidth.
  The host always takes significantly long time to identify the optimal sending rate comparing to the requested completion time.
  The WANs work as black box with unpredictable behaviour for high-speed transmission.
  The WANs always perform random bottleneck link bandwidth allocation among multiple flows leading to uncontrolled completion time.
BltBW (Bottleneck link bandwidth)
RTTprop
BtlneckBuffSize
BDP(Bandwidth Delay Product)
Congestion Notification
HOST
HOST
Transport
Transport
Transport
Transport
1-sending packets with high-speed flows
2-detect an overloaded link with long feeback loop
3-adjust the congestion window size
blind transmission
and detection
variable BDP
BDP= BltBW * RTT
Notes: transport protocols signal and collaborate with the elements along the path to negotiate QoS.

## Slide 6
Problem 2: Unscheduled Traffic
Challenge:
  The host sending large unscheduled traffic without collaboration will lead to the instantaneous congestion in WANs.
  Without traffic patterns of the high-speed flows, the random arrival and departure of cross-traffic without scheduling creates significant fluctuations for available capacity, and it will lead to low bottleneck bandwidth utilization, reduce overall throughput, and prolong the completion time.
WAN
Receiver
Sender 1
Sender 2
....
....
Scheduled
Unscheduled

## Slide 7
Technical Requirements for
Network-collaborated Congestion Control
Host
Edge node
Host
Edge node
collaboration signalling/protocols
collaboration signalling/protocols
traffic patterns
negotiated rates
active network-collaborated
scheduling and acknowledgement
dynamic bandwidth reservation and traffic scheduling
flow control
fast and accurate quantitative feedback
WAN
      A variety of problems about what are specifically in the way for HP-WAN requirements as following shown.
        Host-and-network collaboration signalling or protocols :
          the host should communicate the traffic patterns of high-speed flows to the network.
          the network should make dynamic bandwidth reservation upon different timeframes.
          the edge nodes of network should provide fast and accurate quantitative feedback.
        Active network-collaborated scheduling and acknowledgement:
          the network should provide resource scheduling and traffic scheduling at node nearing source.
          the specific elements along the path should provide active and precise flow control to avoid network congestion.
        Congestion control algorithms:
          improvement of rate-based congestion control algorithms based on the network quantitative feedback at the host.

## Slide 8
Next Steps
Updating the Use Cases I-D (draft-kcrh-hpwan-state-of-art-01) considering the use cases from OTT providers (Google recently added, more OTT examples exist), R&E networks (e.g. CERN) and Public operators (e.g.China Mobile, China Telecom, China Unicom) .
Creating a new Gaps and Requirements I-D with agreed problems.
Scheduling the second interim meeting for HPWAN if required.
Discussions on the mailing list are always welcome.

## Slide 9
Thanks !
Comments and suggestions are welcome.
Notes: north-south traffic需要加入一个手机，表示用户发出的